The following is an outline of the major topics covered in ME 106.

- Mechatronics – What is it all about?

  - Compare/contrast non-mechatronic vs. mechatronic systems

  - Advantages/Disadvantages of mechatronic systems over non-mechatronic systems

  - Fundamental elements of mechatronics (the trees in the forest)

- Important concepts from electronics and circuits

  - Voltage, current, resistance/impedance, power, capacitance, inductance

  - Thevenin’s theorem

  - Voltage division and circuit loading

- Signal sources and signal conditioning

  - Characteristics of signal sources

  - Derivation of frequency dependent voltage divider (AKA, low-pass/high-pass RC filter)

  - Transfer function

    - Magnitude

    - Phase angle

    - Bode diagrams

- The Controller

  - Hardware overview (using the data sheet)

    - Ports, pins, absolute maximums

    - Arduino and Spartan Experimenter Shield

      - Features

  - Programming the controller

    - Digital IO

      - Concept of input and output and configuring pins appropriately

      - Data direction and DDRx register

      - Pull-up resistors and their use

      - Reading from and writing to port pins: Arduino and alternate approaches (PORTx and PINx registers)

    - Bit manipulations

      - Setting a bit

      - Clearing a bit

      - Determining the state of a bit

      - Toggling a bit

- Event Driven Programming

  - Events

  - Services

  - State machines

- Sensors

  - Switches

  - Photoresistor

  - Encoder

- Signal Conditioning

  - Frequency dependent voltage divider (AKA, ‘RC filters’)

    - Transfer function

    - Magnitude and phase angle

    - Frequency response graphs (Bode plots)

    - Filtering a noisy signal

    - High-pass and low-pass

- Power Interface

  - The need to source or sink more current than a microcontroller pin can handle

  - The need to switch on or off voltages beyond what a microcontroller pin can tolerate

  - Diodes

    - Types, their differences, and their applications

    - I-V behavior, forward and reverse bias, PIV

  - Bipolar Junction Transistors

    - Types and their construction

    - Behavior

      - Cutoff

      - Linear

      - Saturation

    - Interfacing between a microcontroller and an actuator

  - MOSFETs

    - Types and their construction

    - Behavior

      - Vgate > Vsource to ‘turn on’ (lower the RDS)

        - For TTL logic level MOSFET: VGS > 5 V fully on

        - For typical power MOSFET: VGS > 10 V fully on

    - Interfacing between a microcontroller and an actuator

  - Switching loads with appreciable inductance

    - Transient voltage suppression

      - Diode

      - Zener diode

    - Relay driver example

- Actuators

  - Permanent magnet DC motor (PMDC) fundamental principles

    - Lorentz force on a moving charge – Force-> Torque proportional to current

      - Torque constant, KT

    - Faraday’s law of induction – a moving coil induces a back EMF

      - Back EMF constant, KE

  - Motor action

    - Rotation direction

    - Commutation

    - Actual construction

  - RC servos

    - Servo construction

    - Servo control

      - PWM

      - Generating PWM with the ATmega328

  - Torque-Speed relationship for a PMDC motor

    - Derivation of torque speed equation for a motor in steady state

      - Important points on the torque speed line

        - Stall torque

        - No load speed

        - Slope of the curve

        - Operating point

    - How to obtain higher speed for a given torque

    - Example from Maxon catalog

  - Motor interfacing and control

    - H-bridge

    - H-bridge interfacing to a microcontroller

  - Stepper motors

    - Stepper operation

    - Stepper construction and wiring

    - Stepper interface and drive

    - Stepper motor dynamics

      - Pull-in torque

      - Pull-out torque

  - Motor sizing

    - Equation for Tpeak

    - Estimating/calculating Tfric and Text

    - Calculating Jtot

    - Motor sizing example

  - Other actuators

    - Linear motors

    - Linear actuators

    - Solenoids

  - Motion control mechanics

    - How to get the motion you want

- Operational Amplifiers

  - Principles and operation

    - Golden rules:

    - Ideal and non-ideal behavior

      - Input impedance

      - Open loop gain

      - Output impedance

  - Amplifier circuits

    - Inverting

    - Non-inverting

    - Summing

    - Buffer

    - Differencing

    - Instrumentation amp

    - Integrator

    - Differentiator

  - Practical limitations

    - Output voltage

    - Output current

    - Gain setting resistors

    - Gain per stage

  - Signal conditioning example

    - Temperature sensor

  - Comparators

    - Comparator action

    - Open collector types

    - Hysteresis

- Digital-to-analog conversion (DAC) and Analog-to-digital conversion (ADC)

  - R-2R ladder DAC

  - Successive approximation ADC

  - Using the ADC system on the ATmega328

    - Example and C code

    - Input range and resolution

- Digital electronics

  - Review of logic functions and logic gate symbols: AND, OR, NOT, NAND, NOR, XOR

  - Combinatorial logic

    - Vote counting circuit example

      - Brute force/quasi logic

      - Truth table methods

        - Sum of Products (SOP)

        - Product of Sums (POS)

        - Karnaugh Map (if covered)

    - Combinatorial logic circuit examples

  - Logic families: TTL and CMOS

    - Switching speed

    - Power consumption

    - Interfacing the logic families together

  - Sequential Logic

    - RS flip-flop

    - D flip-flop

    - JK flip-flop

    - Symbology

      - Triggering

    - Example applications