## Slide 1: Programming Concepts (Part B) ENGR 10 Introduction to Engineering

## Slide 2
IF statement (for one case only)
IF – ELSE statement (for two cases only)
ELSE – IF statement (for more than two cases)
WHILE loop (finite or infinite) statement
Summary
Most commonly used logic statements:

## Slide 3: Functions
The following example shows how to write a function and how to call that function
  MAX_Three  find the maximum of 3 numbers
What is a function?
Function is just a group of code given a name. By grouping and naming it we can reuse it any where in the application without having to rewrite the whole block of code again.
It saves time and reduces the overall code size of your program. But more importantly, if there is a problem you only have to fix it in one place.
Why use a function?

## Slide 4
How to Define a Function in easyC V4
Right click on User Functions and select Add New Function
Name the function (Max_Three and select Return Type (Int)

## Slide 5: Sequential execution of main program which calls the defined function
Main Program
Function
A, B, C, Z1, and Z2 are defined as global variables

## Slide 6: Introduction to Local Variable
The MAX_Three function finds the greatest of the three numbers A, B and C.
These variables were defined as global variables.
Before this function is called, your program must have copied the values into these three variables.
This operation can be done more efficiently by using local variables.

## Slide 7: Program using Function with passing variables
A, B, and C are NOT defined as global variables
x, y, and z are defined as Local variables

## Slide 8: What is a Local variable ?
The value of a local variable is accessible only to the function within which it is defined.
The main function (main program) passes the values into the function and these values are copied into the local variables of the function.
The function doesn’t care what are the names of the variables defined in the main function.
The function does what it should do and then returns the result to the main function.
The values of these local variables are lost after the execution of the function is completed.

## Slide 9: Global Variable Concept
Main Function
Defined Function
Task of the function
A
B
C
Z
A, B, C, and Z are defined as global variables

## Slide 10: Local Variable Concept
Main Function
Defined Function
Task of the function
A
B
C
Z
x
y
max
z
x, y, and z are defined as Local variables

## Slide 11
Mechanical Components – Motors
Motor, continuous rotation of the shaft (3 wire)
Clutch
Make sure the clutch module is always used. It prevents damage to the motor in case of large torque (resistance to motion).
Motor
(Continuous)
Servo
Servo, shaft rotates through a specified angle (3 wire)

## Slide 12
Mechanical Components – Motor (New)
The new motor has two wires (2-wire motors). It can be converted to a 3-wire motor using the controller 29. Ports 1 and 10 on the controller are designated for 2-wire motors only.
2 pins
3 pins

## Slide 13
This chart describes the combination of the motor movement required to perform each maneuver

## Slide 14: How to connect the motor to the Controller?
On the VEX controller you have several ports available so that you can connect not only motors but also other devices and sensors to it.
PORT:
A port is a specific place on the board where we can connect other external devices, so that the two devices in connection can exchange information or data.

## Slide 15
Select Motor, drag and drop on the line between Begin and End
Choose motor number, as connected to the Controller
Max. speed counter clockwise
Max. speed clockwise
Custom speed
Continuous Motor

## Slide 16: How to move a motor?
Use the following statement to move a motor
SetMotor ( 2 , 60 );
This number indicates that the motor is connected to motor port 2 of the total available 10 ports
This number sets the direction and speed of the motor

## Slide 17
Controller (Cortex)
Motor and Servo ports
8 analog and 12 digital ports. Digital ports are used for Limit, Bumper and Ultrasonic sensors
X
connected to the IRB mounted on the robot

## Slide 18
Side view of the VEX Controller
Battery Ports (Square and round connectors)

## Slide 19
Cortex
Two 3-Wire motors to operate the claw and the arm (3-pin)
Two continuous motors to drive the robot (2-pin)

## Slide 20: Program to move the robot forward
Now let us write a program to make the robot move forward for 2 seconds and then stop.
Assume:
Left Motor – connected to motor port 3
Right Motor – connected to motor port 2

## Slide 21
Program to make the motor move forward for 2 seconds and then stop
;

## Slide 22: Clicker Question 3
What value of x will cause the motor for Cortex controller to be stopped: SetMotor(2, x)?
A. 64
B. 127
C. 0
D. 255
E. -127

## Slide 23: Servos
Servo units are similar to motors except that they control position rather than speed.
Servo units have limited range of motion (about 120o)
A value between (-127) and (127) sets
the direction of the servo.
(127) – Extreme counter clockwise direction
(0) – No movement
(-127) – Extreme clockwise direction

## Slide 24
0
127
0o
60o
-60o
Graphical representation of the direction of rotation of the Servo
 Counter-clockwise
Clockwise

-127

## Slide 25: Servo
Similar to the motor the following statement is used to set the servo to turn to a direction.
SetServo ( 5 , 64 );
Indicates the motor port number to which the servo is connected.
This value sets the
direction and the rotation of the servo

## Slide 26
0
-127
127
0o
600
-60o
clockwise 
 Counter-clockwise
SetServo (5 , 64) - EasyC
30o
64
Motor shaft rotates 30o clockwise and then stops

## Slide 27
Program showing how to move the servo continuously

## Slide 28
0
-127
127
0o
60o
- 60o
clockwise 
 Counter-clockwise
Output of the above program
-30o
-64
30o
64

## Slide 29
Mechanical Components - Sensors
Ultrasonic Sensor (Digital)
Bumper Switch Sensor (Digital)
Limit Switch Sensor (Digital)
Sensor blocks

## Slide 30: Introduction to Logic Signals
A logic signal can take on either 0 volt or 5 volt
0v represents “Low state” or “Logic 0”
5v represents “High state” or “Logic 1”
A logic signal can also be called a “digital signal”

## Slide 31: Bumper/Limit Switch
When the switch is not pressed, the robot interprets this value as a 1 (high state).
When the switch is pressed the robot interprets the value as a 0 (low state).
A Bumper/Limit Switch is a digital sensor.
It can distinguish between two states: pressed or not pressed (On or Off)

## Slide 32: Bumper & Limit Switches
Use of the following statement in the program to read the bumper/limit switch.
Bumper = GetDigitalInput ( 2 );
A variable into which the status of the bumper/limit switch will be stored.
This indicates the port number to which the bumper/limit switch is connected

## Slide 33
stores the state of the bumper switch into the variable “bumper”.
checks if there is a contact with an obstacle (switch will be pressed if there is a contact)
motor moves forward as long as there is no obstacle (bumper ==1)
if the switch is pressed (bumper==0), these statements make the robot halt for 1 second
Then the robot turns left for 2 seconds (green arrow is ccw)
Program to make the robot stop and turn for 2 seconds when it hits an obstacle

## Slide 34: Digital Output
The “Digital output” function can be used to control the state of a digital output.
By using this function you can send digital signals (either 0 or 1) to the devices which can accept digital signals.
For example, by using this function you can turn off or on an LED.
1 => 5v => light is on
0 => 0v => light is off

## Slide 35
Drag and drop the Digital Output
List of the output port #
Set the output signal (range), 0 or 1
Port #

## Slide 36: Digital Output
This statement is used in the program to control the devices i.e., send digital signals.
SetDigitalOutput ( 11 , 1 );
Indicates the port number (here port 11) to which the device to be controlled is connected
The digital value to be sent (either 0 or 1)

## Slide 37
Program to make an LED blink continuously

## Slide 38: Ultrasonic Sensor
The measurement is translated into a numeric value from 2 - 100.
Lower signal value corresponds to a closer detected object and vice versa.
The Ultrasonic Sensor is a digital sensor.
The Ultrasonic Sensor uses high-frequency sound waves to detect objects.
It emits a sound wave, measures how long it takes the sound wave to bounce back, and then calculates how far away the object is.

## Slide 39: Ultrasonic Sensor Connections
Ultrasonic Sensor
VEX Controller
Digital Output port
(Interrupt port)
Input
Output
Digital Input port

## Slide 40: Ultrasonic Sensor
Sensor connected to input port 5
Sensor connected to output port 6 through which it receives digital control signals from the controller.
The following statement starts an ultrasonic sensor i.e., the sensor starts sending and recording the sound signals.
StartUltrasonic ( 5, 6 ) ;
Select start

## Slide 41: Ultrasonic Sensor
Variable into which the translated value is stored
Input to Ultrasonic port #5
The sensor is connected to output port # 6 on the controller
The following statement is used to read a value from the sensor
Range = GetUltrasonic ( 5 , 6 );
Select Get option
Define variable Range, (2-100)

## Slide 42
Changing Input port to Output port
Digital ports taken by the IRB
Change port 6 from input to output by clicking on the circle
Edit Config

## Slide 43
Input to Ultrasonic sensor connected to output port 6 on controller
Output from Ultrasonic sensor connected to input port 5 on controller
Checking if the obstacle is near or far

## Slide 44
Analog Signals
For the VEX controller, an analog signal can take any value between 0v and 5v.
0v is represented by a value 0
5v is represented by a value 1023 (210)
All other voltage levels between
0v and 5v are represented by the
numbers between 0 and 1023.
1023
5v
0
0v
511
2.5v

## Slide 45: Light Sensor
A light sensor is an example of an analog sensor.
A light sensor reads the intensity of light of an area, translates the reading into a single numeric value, and sends that value to the robot.
The range of values used by this sensor is
0-1023
The higher the value, the darker will be the area and vice versa.

## Slide 46: Light sensor
The following statement is used to read the analog signal from a light sensor.
light = GetAnalogInput ( 1 ) ;
A variable named “light” into which the reading (0-1023) from the light sensor is stored
Indicates the port number (here port 1) to which the light sensor is connected

## Slide 47
Program to make the robot move towards the moving light source
If light intensity is more on the left side, the robot turns toward the left side
If light intensity is more on right side, the robot turns toward the right side
If light intensity is the same on both sides, the robot moves forward
ELSE IF is used for more than 2 cases

## Slide 48: Optical Shaft Encoder
The optical shaft encoder is a digital sensor. It is used to measure rotational movement.
Disc with 90 equally spaced slots
As the disc rotates, an infrared light sensor is used to count the number of slots passed.
A count of 90 makes one revolution.

## Slide 49: Optical Shaft Encoder
The following statement is used to start the encoder counting.
This number indicates that the encoder is connected to interrupt port # 2 on the VEX controller
StartEncoder ( 2 ) ;

## Slide 50: Optical Shaft Encoder
The following statement is used to get the present count value from the encoder.
Count = GetEncoder ( 2 ) ;
A variable named “count” into which the present count value will be stored
Interrupt port # 2 to which the Encoder is connected

## Slide 51
PresetEncoder ( 2, 20) ;
This statement is used to make the encoder start counting from a given number (here 20) instead of from zero.
Example
Write a program to make the robot move for 1 meter and then stop.
Assume 5 turns of the wheel = 1 meter

## Slide 52
Program to make the robot move forward for 1 meter
Presetting the encoder to 20. Count value starts from 20.
if count reaches 470 the robot stops.
470 = 450 (count for 5 turns x 90) + 20 (initial value)
0
0