## Slide 1: Programming Concepts Part C GOTO_Beacon ENGR 10 Introduction to Engineering

## Slide 2
Download the GOTO BEACON program from the E10 website, Robot lab section,
New controller (Cortex)

## Slide 3
Main() for GOTO_Beacon Program
Note: you need to change freq for the beacon you want to find!
Global
Variables
Call three functions
Infinite loop

## Slide 5
While Loop (1==1)
{
Read_PD(); //read 8 Photo-detector outputs
find_max(); //find the max detector output
move(); // move to the direction of max PD
}
PD7
PD0
PD4
Right side
Left side
The main body of the GOTO_Beacon program
is an infinite loop with three functions in the loop

## Slide 6
Read_PD()
This function reads the intensity of all 8 Infrared Photo-Detectors and stores the intensity (0 to 1023) into PD0~PD7 variables. It also produces the sum of all 8 readings (PD_sum). The sensing sensitivity is set by expose_time.
find_max()
This function determines which variable (among PD0~PD7) has the greatest value. The PD number is saved in the variable max_no.
This function reads the intensity of either 1kHz or 10kHz infrared signal depending on the setting of digital output port 10 on Cortex, (0=1kHz , 1=10kHz). You should set the digital output port #10 to the intended frequency before this function is called.

## Slide 7
move()
PD7
PD0
PD4
Stop if PD_sum > stop_level (6000)
Slows the forward motion to slow_speed if PD_sum > slow_level (5000)
If PD_sum < Ambient (noise level, 200), the robot spins at the speed spin_speed (50). If PD_sum > Ambient (beacon is in view), go forward at speed of forward_speed (35).
Turns the left wheel faster if max_no (PD #) <4
Red beacon
Turns the right wheel faster if max_no > 4,
same speed if max_no = 4

## Slide 8
Read_PD() Function

## Slide 9
Find maximum intensity

## Slide 10
find_max() Function

## Slide 11
Move the robot

## Slide 12
Move() Program
PD_sum<200, no beacon in sight, robot spins
PD_sum >5000, robot slows down, beacon is close
PD_sum >6000, very close to beacon, robot stops
Robot moves toward beacon

## Slide 13
limit_pwm() Program

## Slide 14
PD2 reads max intensity  max_no = 2  error = 4-2=2  steer=error*steer_sensitivity=2*20=40
Motor1 speed = 0+40+35=75,
Motor10 speed=0+40-35=5,
if motor 1 is on the left side the robot turns right
Cortex Controller

## Slide 15
Initialization
While state==1
Read PD();
Find Max();
Move ();
Somewhere here, when red beacon is found, state=2.
No infinite loop in all blocks!
While state==2
Try to turn off red beacon. when confirmed, state=3
While state==3
Go to green
When found, state=4
How to add to the GOTO_beacon program to perform the required task?
Use state variable !
Find red beacon
Find green beacon

## Slide 16
While state==4
Capture green (turn off) ,
When confirmed.
state =5
STOP
While state==7
GO home,
When confirmed.
state =6

## Slide 17
E10 robot, bumper switches, it wonders

## Slide 18: IR Receiver Board

## Slide 19
amplifier
Tuning circuit
From previous stage
To next stage
Beacon Frequency Selection (filter)
AD14 Freq select (0=1kHz, 1=10kHz)

## Slide 20
Infrared Detectors
Selector
1
1
0
To next stage
counter
LEDs
AD16 Counter reset
AD15 pulse
IR Detector Selection
1
1
0
Count output set to zero
Get ready to count
Increment count (0 to 1 transition)

## Slide 21
amplifier
Tuning circuit
From previous stage
To next stage
Beacon Frequency Selection (filter)
AD14 Freq select (0=1kHz, 1=10kHz)

## Slide 22
Exposure Control Circuit
AD15
From previous stage
To AD1
(VEX Analog input)
Amplifier
1
Clear ‘film’ (discharge C14)
0
Open ‘shutter’ (allow C14 to charge)