## Slide 1: Ethics in Engineering
Lecture 3/3

## Slide 2
The Challenger Disaster (January 28, 1986)
An important and major case….

## Slide 3
Challenger Launch

## Slide 4
Challenger Crew
(front row) Michael J. Smith, Dick Scobee, Ronald McNair
(back row) Ellison Onizuka, Christa McAuliffe, Gregory Jarvis, Judith Resnik
http://images.jsc.nasa.gov/luceneweb/caption_direct.jsp?photoId=S85-44253

## Slide 5
Orbiter containing flight deck and crew
Challenger disaster photos copied and text adapted from Aerospaceweb.org (2004) Space Shuttle Challenger Disaster, Retrieved November 3, 2008 Aerospaceweb.org, Web site: http://www.aerospaceweb.org/question/investigations/q0122.shtml
The primary component of the vehicle assembly was the Orbiter, the reusable, winged craft containing the crew that actually traveled into space and returned to land on a runway.
Technical Details

## Slide 6
The Orbiter alone did not generate enough thrust or carry enough fuel to get into orbit.
Additional thrust was provided by two large Solid Rocket Boosters (SRB)
  Attached to the side of the External Tank by means of two struts

## Slide 7: Once the two solid rocket boosters lift the Shuttle to an altitude of about 45,760 m (roughly 28.4 miles), they are jettisoned
Left Solid Rocket Booster
Right Solid Rocket Booster
External Tank
Three main engines of the orbiter

## Slide 8
http://www.spaceref.com/news/viewnews.html?id=1399
SRB built in Utah and shipped by train to launch pad
https://www.youtube.com/watch?v=4-jbIYjHOmc

## Slide 9
https://www.youtube.com/watch?v=4-jbIYjHOmc

## Slide 10
https://www.youtube.com/watch?v=4-jbIYjHOmc

## Slide 11
Challenger disaster diagrams copied and text adapted from Aerospaceweb.org (2004) Space Shuttle Challenger Disaster, Retrieved November 3, 2008 Aerospaceweb.org, Web site: http://www.aerospaceweb.org/question/investigations/q0122.shtml
Two-thirds of the External Tank was filled with liquid hydrogen; the top third with liquid oxygen
This fuel supplied the three main engines of the Orbiter until about 8 1/2 minutes after liftoff
Then the External Tank would be jettisoned at about 111,355m (roughly 69.2 miles) .

## Slide 13
NASA Images

## Slide 14
Challenger lifts off at 11:37 AM

## Slide 15
Just less than 73 seconds after lift-off, smoke was seen billowing out from the right solid rocket booster followed by several explosions

## Slide 16: Challenger disintegrated 73 Seconds into flight
Smoke plume of the Space Shuttle, Challenger at 73 seconds after launching

## Slide 18: The Failure that Caused the Disaster
O-ring seal in the right SRB failed to remain sealed.
O-ring failure allowed a flare of pressurized hot gas from the SRB
Resulting flames burned the adjacent SRB attachment hardware -- the strut -- and ignited the liquid hydrogen and oxygen in the external fuel tank.
Various subsequent structural failures caused orbiter to break apart

## Slide 19: SRB
http://history.nasa.gov/rogersrep/v1p56.htm
Solid Rocket Booster (SRB)

## Slide 20
http://galaxywire.net/2009/07/06/solid-rocket-booster-cutaway-view/

## Slide 21: SRB
http://engineeringfailures.org/?p=85

## Slide 22: SRB
http://www.carpinner.com/solid-rocket-booster-diagram/

## Slide 23
http://www.spaceflightnow.com/shuttle/sts135/110410flow/

## Slide 24
Close-up view of the rubberized O-ring seals within the Solid Rocket Booster casing. These seals were intended to prevent a leakage of hot gases, but on Mission 51L they failed spectacularly. Photo Credit: NASA

## Slide 25: Design of the Solid Rocket Booster
The four segments of each booster were joined by what is known as tang and clevis joints.
Tang
Clevis

## Slide 26
O-Ring
Slots

## Slide 27
https://religiousreason.wordpress.com/2014/10/10/boldly-going-where-no-one-has-gone-before/

## Slide 28
As pressure increases inside the SRB, it pushes the tang away, but also flattens out the O-ring to seal the gap.
Gas Pressure
O-rings

## Slide 29
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications

## Slide 30
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications
Clevis

## Slide 31
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications
Clevis

## Slide 32
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications
Clevis

## Slide 33
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications

## Slide 34
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications
O-Ring Seal Flattens

## Slide 35
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications
Clevis
O-Ring Seals
Don’t Flatten

## Slide 36
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications
Clevis
“Blow by” Begins

## Slide 37
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications
“Blow by”

## Slide 38
With temps in 20os overnight and 36o at launch, it was the coldest day in history that a shuttle had been launched.
This picture was taken on the morning of the Challenger launch January 28, 1986.

## Slide 39
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications

## Slide 40
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications

## Slide 41
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications

## Slide 42
https://www.youtube.com/watch?v=4-jbIYjHOmc

## Slide 43
https://www.youtube.com/watch?v=nspP1YFftAY – Boston Science Communications

## Slide 47
One reason the Challenger disaster occurred was due to a faulty factory joint.
True
False

## Slide 48: Actually the Case is Much more complex
Rather than only looking at the facts after the disaster – let’s look at what was happening in real time

## Slide 49
Roger Boisjoly, chief O-ring engineer at Morton Thiokol, had warned his colleagues that O-rings lose their resiliency at relatively low temperatures
August 19, 1985 - NASA Level I management briefed on booster problem
April 25, 1938 – January 6, 2012

## Slide 50: Night before the Launch
Engineers, including Roger Boisjoly, could not supply conclusive data regarding at what temperatures it would be unsafe to launch the Challenger.
According to a Marshall Space Flight Center manager no one had performed a statistical analysis correlating past O-ring performance with either temperature or leak check pressure

## Slide 51
Each of the four launches below 61o showed thermal distress to at least 1 O-ring

## Slide 52: NASA Manager Anxious to Launch
Economic considerations
  Delays are costly
  Limited windows for space probes or satellites
Political pressures
  Competition with European Space Agency & Russians
  Need to justify budget requests
  Possible pressure to launch before presidential speech
Scheduling backlogs
  Many delays in previous shuttle mission
  Several days of bad weather, electronic switch malfunction
Notes: NASA proposed year-round launches, up to 24 launches per year!!!

## Slide 53
http://aam.govst.edu/projects/csexton/student_page5.htm

## Slide 54: Final Decision
After much back and forth discussion with NASA, Jerald Mason told Morton Thiokol supervising engineer, Robert Lund: “take off your engineering hat and put on your management hat.”
Without firm figures to determine that the launch was unsafe, the earlier recommendation to delay the launch was reversed.
Rogers Commission, Report to the President by the Presidential Commission on the Space Shuttle Challenger Accident (Washington, D. C.: June 6, 1986), pp. 772-773.

## Slide 55
Do you think NASA should have launched?
Is there a clear moral issue here?
Did NASA take unnecessary risks because of external pressure?
Did M-T engineers violate their duty to put public safety first?

## Slide 56: Was there a conflict between…..
Engineering Code of Ethics and
Upholding high standards of professional competence and expertise
Holding paramount the health, safety & welfare of the public
Prima Facie Duties for Management?:
A. Maximizing the well-being of the organization
B. Upholding organizational employee morale and welfare

## Slide 57: Quotes from Investigation
Larry Sayer – Engineer at Morton Thiokol
[W]e had a very weak engineering position when we went into the telecom
Ben Powers – Marshall Space Flight Center
I don‘t believe they did a real convincing job of presenting their data … The Thiokol guys even had a chart in there that says temperature of the O-ring is not the only parameter controlling blow-by. In other words, they‘re not coming in with a real firm statement. They‘re saying there‘s other factors. They did have a lot of conflicting data in there.

## Slide 58: More about Internal Discussions
Unusual situation
  First time in the life of project that a contractor had made a recommendation not to launch. Usually NASA called for a delay
NASA engineers did not know that the final M-T “Launch” decision was not unanimous
While concerns about O-rings had been raised, the concerns had not been specifically about launching a low temperatures – NASA taken somewhat by surprise

## Slide 59: Benefit – Cost in Decision Making
Wouldn’t the NASA manager think the potential costs were too great?
  Human lives
  His reputation
  Criminal charges
  100% of the blame on him
  Suspension of the shuttle program
Wouldn’t the M-T managers come to the same conclusion?

## Slide 60: Rogers Commission Findings
“…failures in communication… resulted in a decision to launch 51-L based on incomplete and sometimes misleading information, a conflict between engineering data and management judgments, and a NASA management structure that permitted internal flight safety problems to bypass key Shuttle managers.”
Rogers Commission report (1986). "Report of the Presidential Commission on the Space Shuttle Challenger Accident"

## Slide 61: If you want to Dive into This Case More Deeply
Elements of whistle blowing
Many more uncertainties associated with technical issues – conflicting data
Issues of poor communication
Poor decision making based on “group think”

## Slide 62
In the cases we’ve considered before, we’ve frequently seen that ethical dilemmas often appear as a hard choice. You have to choose between the lesser of two evils. In the Challenger disaster, obviously the lesser of two evils choice should have been to delay the launch.

## Slide 63: A final Question
Can you suggest a creative middle way solution between the disastrous decision to launch the Challenger on January 28, 1986 and to postpone it? The creative middle way solution should address both the goal of eliminating the risk of the malfunctioning O-rings and at the same time allow NASA to keep its commitments for on-schedule launches.

## Slide 64: Final Summary
2. Ethical problem solving, whether personal or professional, strives to find creative ways to reconcile conflicting goals.
1. Engineering professional goals, such as protecting public safety and client and employee honesty, lead to the trust and progress of the engineering profession