## Slide 1
The Blade design
Tutorial

## Slide 2: Various Blade designs

## Slide 4: The Blade Shape
Design groups should conduct a thorough search of the Internet to obtain information on wind turbine blade design and efficiency. Based on your research, decide on the number and general shape of the blade.
Constraints:
Total dimension of the turbine blade assembly (diameter of the swept area) should not exceed 6 inches.
The propeller must fit within the 6 inch diameter circle
6 in.

## Slide 5: The Blade Shape
Blade length, measured from the edge of the hub, should not exceed 2.5 inch.
Blade height is limited by the thickness of the hub. It should not exceed 0.25 inch.
There are no constraints on blade width (.7 dimension)
The tutorial in the following slides is based on the blade geometry and shape shown above.
.7 in
.25 (hub thickness)
Height
Length 2.5 in. max allowed
Width (up to you)

## Slide 6: Modeling the Wind Turbine Blade
The hub for the wind turbine blade has been modeled using SolidWorks. Use the following link to download the file “Hub” from Canvas in Wind Turbine Module

## Slide 8: Create the first Reference Plane
Select Sketch and choose the top surface of the hub to draw.
Exit the sketch
Draw a line from the center
Dimension the line 0.25 inch

## Slide 9: Create the first Reference Plane
Click on the icon to create the reference plane
The reference plane passes through the point and is perpendicular to the line
Select the end of the line as the first reference.
Select the line as the second reference

## Slide 10: Creating the Blade Profile at the Hub
Select Sketch and choose the first reference plane to draw the blade profile at the hub
From the View Orientation menu choose the Normal To option
Do not be concerned with the size of the reference plane; it is infinitely large.

## Slide 11: Creating the Blade Profile at the Hub
Select Convert Entities to project the hub onto the sketch plane to use as a reference for drawing the profile. Select the top and bottom edges as shown
Make sure you select edges and not surfaces. Zoom in for better view

## Slide 12: Creating the Blade Profile at the Hub
Draw a vertical line from the midpoints of the projected lines
Draw two more vertical lines on either side of the previous line
Dimension both lines with respect to the middle line, 0.35 inch. The 0.7 inch distance represents the width of the blade at the hub. (This is a design variable; you may choose a different value.)

## Slide 13: Creating the Blade Profile at the Hub
The profile is constructed within the 0.7” by 0.25” envelope
0.7
0.25
Construct a diagonal line
In this design, 5 points are selected. The end points of the diagonal line must be included in your point selection. The location of other points are up to you and will determine shape of the profile, which in turn will affect the power output.
Pt. 1
Pt. 2
Pt. 3
Pt. 4
Pt. 5
Use the spline command to draw the curved portion of the profile

## Slide 14: Creating the Blade Profile at the Hub
The shape of the spline curve could be modified by selecting any point and dragging it to a new position
Make sure the curve does not protrude beyond the surface of the hub
Delete all construction lines before exiting the sketch

## Slide 15: Creating the Blade Profile at the Tip
Create the second reference plane to draw the tip profile
This arrangement will create a blade sweep area of 6 inch in diameter. It is the maximum blade size allowed.
Select reference plane option, select the first reference plane and enter the distance between the tow planes, 2.75 inch.
2.75 in.
Reference plane to draw the tip profile

## Slide 16: Creating the Blade Profile at the Tip
Select Sketch and choose the second reference plane to draw the tip blade profile.
From the View Orientation menu choose the Normal To option.
Project the blade profile at the hub and the bottom surface into the current sketch plane. This is used as a reference to draw the tip profile

## Slide 17: Creating the Blade Profile at the Tip
Draw a vertical line from the midpoints of the projected diagonal line.
Draw two more vertical lines on either side of the previous line
Dimension both lines with respect to the middle line, 0.175 inch. The 0.35 inch represents the width of the blade at the tip, half of the width at the hub. This is also a design variable; you may choose a different value

## Slide 18: Creating the Blade Profile at the Tip
Use the Spline and line commands to construct the tip profile. Follow the same procedure as the profile at the hub.
Delete all construction lines before exiting the sketch
This shows the two blade profiles, at the hub and at the tip

## Slide 19: Creating the Blade - Loft
Select the Loft command and choose the two profile
Hub profile
Tip profile

## Slide 20: Rounding the Blade Edges – Fillet Command
The blade edges should be rounded in order to obtain a model with clean edges. The 3D printer is not capable of modeling sharp edges.
Select the Fillet command, choose the edges and provide a radius for the fillet.

## Slide 21: Fillet
Select the front edge
Assign a value of 0.015 inch to the front edge
Select Fillet again and choose the back edge and assign a value of 0.01 inch

## Slide 22: Completing the Rotor – Pattern Command
Select the Circular Pattern command
Select the axis of the circular pattern, choose the circle
Choose the number of the blades
Check the Equal spacing box for full 360 deg.
Select the blade and the fillets

## Slide 23: Embossing the Hub
In order to identify your blade it has to be embossed with your group number and lab. section.
Select Sketch and choose the top surface of the hub. Use the Text command and write your group number (G4) and lab. section number (S8). Make sure the text is not too close to the hole.

## Slide 24: Embossing the Hub
Select the text and right click to modify, move, scale,….
Make sure the Keep relations is checked off
Select the From and To to move the text

## Slide 25: Embossing the Hub
Extrude the text by 0.025 to 0.03 inch

## Slide 26
The Rotor