## Slide 1: Heat Generation in Electronics
Thermal Management of Electronics
Reference:
San José State University
Mechanical Engineering Department

## Slide 2: Heat in Electronics
Heat is an unavoidable by-product of operating electronics
Effects of increased temperature in electronics
  Decreased reliability
  Parametric changes may occur in an electronic device’s components

## Slide 3: Power Dissipation
Current flowing through active and passive components results in power dissipation and increased temperatures
The amount of power dissipated by a device is a function of:
  The type of device
  The geometry
  The path from the device to the heat sink

## Slide 4: Components Where Power Dissipation Occurs
Passive Devices
  Resistors
  Capacitors
  Inductors
  Transformers
Active Devices
  Transistors
  Integrated Circuits
Interconnections

## Slide 5: General Theory
Power dissipated will be a function of the type of current that it receives
For DC:

## Slide 6: General Theory
For AC:

## Slide 7: Resistors
Symbol
Power Dissipated

## Slide 8: Temperature Coefficient of Resistance (TCR)
TCR characterizes the amount of drift that takes place in resistance values over temperature change
TCR usually has such a small effect that (even over large temperature gradients) that it can be ignored for resistors

## Slide 9: Capacitors
Symbol
The ideal capacitor would not dissipate any power under a DC current
A real capacitor can be modeled with the equivalent series circuit below:

## Slide 10: Capacitors
There will be power dissipated due to the equivalent series resistance (ESR)
Power dissipation due to equivalent series inductance is negligible compared to ESR

## Slide 11: Inductors and Transformers
Inductor symbol
Transistor symbol
Two types of resistance associated with these devices
  Winding
  Core

## Slide 12: Resistance for Inductors and Transformers
Winding Resistance – Resistance that occurs due to the winding on the component
Core Resistance – Losses that occur due to use of a ferromagnetic core
  Hysteresis Loss – Power dissipation due to the reversal of the magnetic domains in the core
  Eddy Current Loss – Heat generated from the conductive current flowing in the metallic core induced by changing flux

## Slide 13: Active Devices
Power dissipation for all standard-product active integrated circuits can be obtained from:
  Device data sheets
  Calculated from laboratory measurements
Bipolar devices – power dissipation is constant with frequency
CMOS devices – power dissipation is a 1st order function of frequency and 2nd order function of device geometry

## Slide 14: Power Dissipation in a CMOS Gate
Power consumption is composed of three components:
  Switching power
    Results from charging and discharging of the capacitance of transistor gates and interconnect lines during the changing of logic states
    Comprises 70-90% of the power dissipated

## Slide 15: Power Dissipation in a CMOS Gate
  Dynamic short-circuit power
    Occurs when pull-up or pull-down transistors are briefly on during a change of state in the output node
    Comprises 10-30% of dissipated power
  DC Leakage
    Comprises 1% of dissipated power

## Slide 16: Interconnections
Interconnections are the connections between components
Power dissipated can be found with Joule’s Law where resistance of the interconnection is given by:

## Slide 17: Wire Bonds
Low power devices (i.e. logic and small analog devices) usually have bonds fabricated from gold or aluminum with a diameter of .001 inch
  Negligible power is dissipated by a single bond but when many bonds exist these elements should not be ignored
High power devices usually have aluminum bond with diameters ranging from .005 to .025 inches
  Large amounts of power are dissipated from these bonds

## Slide 18: Wire Bonds

## Slide 19: Ribbon Bonds

## Slide 20: Package Pins
Package pins are the physical connector on an integrated circuit package that carries signals into and out of an integrated circuit
Pins are made from low-resistance metal and may be enclosed in glass or ceramic bead
Power dissipate can still be calculate with the relationship outlined for other interconnections
Notes: <number>

## Slide 21: Package Pins

## Slide 22: Substrates
Many different metallizations can be used for interconnections on substrates
Each metallization will have its own resistance that will dissipate power
Sheet resistivity is used in calculation due to the fact that conductors are much wider than they are thick

## Slide 23: Substrates
The resistance of a substrate can be found with the sheet resistivity
Resistivity of the conductors will vary with temperature (TCR may be important in some substrate calculations)

## Slide 24: Various Substrate Constructions

## Slide 25: Substrate Metallization Properties

## Slide 26: High-Frequency Loss
DC is evenly distributed throughout a cross section of wire
When frequency increases charge carrier move to the edges because it is easier to move in a conductor in the edge
Resistance increases due to the distribution of charge carriers